## Slide 1: Polymeric Materials Molecular View
MFG 355

## Slide 2: Level of focus – Molecular View
Molecular features at the atomic level
  Bonding
  Chemistry
  What is a polymer
  Polymerization reactions
    Addition polymerization
    Condensation polymerization

## Slide 3: Fundamentals of Matter
Metals
Non-Metals
(Give up electrons)
(Take on electrons)
3

## Slide 4: Bonding (attractions)
Ionic – Metal with Non-metal
Cl
Na
+
-
Transfer of electron

## Slide 5
+
-
+
-
-
+
-
+
+
-
+
-
-
+
-
+
Ionic Bonds
Negatively Charged Non-Metal Ion
Positively Charged Metal Ion
Part
Crystal structure showing charged metal and non-metal ions and the ionic bonds between them

## Slide 6: Bonding (attractions)
Metallic – Metal with Metal
Cr
Fe
+
+
Sea of electrons

## Slide 7
+
+
+
+
+
+
+
+
Sea of electrons
Positively Charged Metal Ion
Part
Crystal structure showing charged metal ions and the sea of electrons between them
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 8: Bonding (attractions)
Covalent – Non-metal with Non-metal
Shared electrons
Cl
Cl

## Slide 9: Periodic Table of the Elements
Metals
Non-Metals
Ceramics
(Ionic Bonds)
Metals
(Metallic Bonds)
Polymers
(Covalent Bonds)

## Slide 10: Solid Materials – 3 Types
Ceramics
Metals
Polymers
These differ, at the most fundamental level,
in the types of bonds between the atoms

## Slide 11: Now, a little more chemistry
Don’t be afraid!

## Slide 12: Atomic Orbitals
Electrons
  Shells (n=1,2,3,4,5)= rows on periodic table
  Orbitals (s,p,d,f) = columns on periodic table
s
p

## Slide 13: Basic Organic Chemistry
Atomic Carbon has 4 electrons in its outer shell
All organic molecules contain Carbon
Valence bonds (number of bonds formed)
  Carbon=4, Nitrogen=3, Oxygen=2, Chlorine=1, Hydrogen=1

## Slide 14: Basic Rule
In molecules, the atomic bonds change to allow bonding with the approaching atoms
  If 4 atoms approach, all 4 atomic orbitals change to equivalent molecular orbitals and spread apart
C
These are called sp3 molecular orbitals and they form σ molecular orbitals (cylindrical)

## Slide 15: Basic Rule
  If 3 atoms approach, 3 atomic orbitals change to equivalent molecular orbitals (called sp2) and one atomic orbital does not change (pz)
When carbon only bonds with three other atoms, the unchanged atomic orbital (pz) overlaps above and below to make one molecular bond (a π-bond)

## Slide 16: Bonding (attractions)
Function of
distance between atoms
Bond Length (average)
Distance between atoms
System energy
Bond energy
Ι
Energy neutral line

## Slide 17: Resin Rules
Resin Rule: Polarity occurs when certain highly electro-negative atoms are present in the molecule
  Electronegative atoms withdraw electrons from their neighboring atoms
  Highly electronegative atoms are: F, O, N, and Cl
  Attractions between polar areas on molecules or atoms result in secondary bonds
  These bonds are much weaker than the three types of primary bonds (ionic, metallic, covalent)

## Slide 18: Bonding (attractions)
C
Secondary bonds
  Polar bond/Hydrogen bond
    One atom in a covalent bond is more negative than the other
    Atoms that cause polar bonding = F, O, N, Cl
    Electrons spend more time around the more polar atom
O
δ+
δ-
Unequal sharing
Partial charges

## Slide 19
Polarity – Magnet Analogy
N S
S N
S N
S N
d+
d+
d-
d-

## Slide 20: Secondary Bonds
Attractions between polar areas on molecules or atoms result in secondary bonds
  These bonds are much weaker than the three types of primary bonds (ionic, metallic, covalent)
Distance between atoms
System energy
Primary bond energy
Energy neutral line
Primary bond
Secondary bond
Secondary bond energy

## Slide 21: Bonding in polymers by polarity
Polar areas on the polymers attract oppositely charged polar areas on other molecules
d-
d-
d+
d+
Attacked by water molecules
Polyester
Secondary bond

## Slide 22: Polymers
Polarity in polymers

## Slide 23
―
―
―
―
―
―
0
2
1
3
4
5
6
Weight gain (%)
│
│
│
│
│
0
50
100
150
200
250
Exposure time (hours)
□
□
□
□
□
Vinyl ester resin
●
●
●
●
●
Polyester resin
Weight gain in water of polyester and vinyl ester resins because polyester is more polar than vinyl ester

## Slide 24: Bonding
Non-polar areas also attract each other
  Hence areas within molecules attract other areas that are similar
  Non-polar attractions are even weaker than polar attractions
  Like-attracts-like rule

## Slide 25
Bonding – Coupling Agents
Fiberglass
Sizing or coupling agent
Nonpolar regions (weak attraction)
d-
d-
d+
d+
d+
− A highly polar molecule
− Largely non-polar with a polar end
Polyester
− Mixed polar/non-polar
Polar
regions
attract
Non-polar

## Slide 26: Now, since you know about atoms and molecules, it is time for a little story
Two atoms were walking along the street and the first atom said to the other:
“I’ve lost an electron.”
The other said, “Are you sure?”
The first answered, “Yes, I’m positive!”

## Slide 27: Functional Groups – Determining Properties

## Slide 28: Resin Rules
Resin Rule: Aromatic groups change the mechanical, thermal, flammability and weathering properties of a polymer.
  Aromatic (benzene) rings are hard, flat entities
  Aromatic rings increase stiffness and strength of the polymer, especially as they are integrated into the backbone or into a network
  Aromatic rings increase thermal stability
  Aromatic rings decrease flammability and smoke
  Aromatic rings decrease UV stability

## Slide 29: Polymers − Molecular shape
Aromatic − Contains the benzene group (sometimes called phenyl group)
  Increases stiffness
  Increases strength
  Increases non-flammability
Aliphatic −Does not contain the benzene group
  Increases flexibility
  Increases toughness
  Increases weatherability

## Slide 30
a) Aromatic group (benzene)
b) Polystyrene (pendant
aromatic)
c) Epoxy (aromatic backbone)
d) Phenolic (aromatic network)
H
H
H
H
H
H
Aromatic molecules

## Slide 31: Flammability
10
20
30
40
Vinyl Ester
Epoxy
FR Polyester
Phenolic
(ASTM E-162 for thermoset
composites)
Vinyl Ester
Epoxy
FR Polyester
Phenolic
(ASTM E-662 for thermoset
composites)
100
Specific Optical Density
Flame Spread Index
200
300
400
500
600

## Slide 32: Resin Rules
Resin Rule: Materials containing halogen atoms (F, Cl, Br, I) have good flame retardance properties.
  Smoke evolution is increased with halogens

## Slide 33: Halogenated polymers
Polyvinyl chloride (PVC)
Polytetrafluoroethylene (PTFE)
Brominated Epoxy

## Slide 34: Polymers
Polymers can be natural (like wood, cotton, wool, leather)
Polymers can be man-made (plastics)
Polymers can be easily shaped (molded)
Polymers have other advantages over ceramics and metals

## Slide 35: Materials Taxonomy

## Slide 36: Polymers
Made from small molecules (monomers) which are linked together
  “mono” means one
  “mer” means unit
The linked monomers form a chain-like structure called a polymer
  “poly” means many

## Slide 37: Polymers
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
Monomers
Polymer
Covalent
Bonds
The links are the covalent bonds between the atoms

## Slide 38: Polymers
Carbon based and silicon based
  Almost all polymers are based on carbon
  Silicones and related polymers are the only silicone based polymers

## Slide 39: Addition Polymerization
Mechanism
  Monomer in vessels (temperature and pressure)
  Initiator—free radicals
  Attack C=C (π bond)
  Bond and make new free radical
  New π bond reaction
  New free radical created
  Continuation
  Termination

## Slide 40
Addition Polymerization

## Slide 41: Addition Polymerization
Initiation and growth

## Slide 42: Addition Polymerization
Chain Termination—Unreacted end, another chain

## Slide 43: Addition Polymerization
Chain Termination—Unreacted Peroxide

## Slide 44: Addition Polymerization
Chain Termination—Ozone Quench

## Slide 45: Addition Polymerization -- Variables
Catalysts (not the same as initiators)
  Usually metal or metal oxides
  Give a place for the growing molecule to be located
  Increase effectiveness of collisions (reactions)
Concentrations (pressure)
Temperature (high)
Contaminants
Other monomers

## Slide 46: Addition Polymerization
Copolymers from Addition Polymerization
  Block Copolymer
  Random Copolymer
  Regular Copolymer
  Graft Copolymer

## Slide 47: Condensation Polymerization
Mechanism
  Monomers (2)
    Each has two reactive sites
  Monomer ends react
  Condensation
    Removal of condensate
  Chain termination ends reaction

## Slide 48: Polyester polymerization
Monomers
Glycols G
(di-alcohols)
Acids A
(di-acids)
G
G
G
G
A
A
A
A
A
Polyester polymer

## Slide 49: Polyester polymerizationn
One end of the di-acid (the OH group) reacts with one end of the glycol (the H group) to form water (H−OH)
  The water separates from the polymer and condenses out as a liquid
  These type of polymerization reactions are called condensation reactions

## Slide 50
HO―G―OH
Glycol
O
H
C
A
C
O
H
O
O
Di-acid
Step 1: Monomers react
+
Step 2: New molecule reacts with new monomers
O
O
HO―G―O―C―A―C―OH
+
HO―G―OH
Glycol
O
H
C
A
C
O
H
O
O
Di-acid
+
Ester
Ester
Ester
O
O
O
O
HO―C―A―C―O―G―O―C―A―C―O―G―OH
Condensation Polymerization of a typical polyester
HO―G―O―C―A―C―OH
O
O
Ester
New bond
+ H2O
+ 2 H2O

## Slide 51: Condensation Polymerization
Monomers/Polymers

## Slide 52: Addition vs. Condensation
Polymer Growth Mechanism
Dependence on previous step
Initiator needed
Type of monomer
Number of active sites (functional groups) per monomer
Number of different types of monomers needed to form polymer
By-product formed
Basic (polymer repeat unit) representation
Polymer chain characteristics
Branching
Chain reaction
Yes—dependent sequential events
Yes
Contains carbon-carbon double bond
1
1
No
Monomer without the double bond and with bonds on either side
A few, long chains
Possible
Step-by-step reactions
No—independent events
No
Has reacting bifunctional groups on the ends
2
2 (usually)
Yes (usually)
Two monomers joined (without condensate)
Many not very long chains
Unlikely
Addition polymerization
Condensation polymerization

## Slide 53: Thank You
Remember the molecules