## Slide 1: Thermoforming
MFG 355

## Slide 2: Thermoforming Characteristics
Not dependent on extrusion/melting
Sheets are used as the starting material
  This increases the raw material cost over “melted” processes
  High raw material waste
    Recycled but not at original cost

## Slide 3: Thermoforming Variations
Vacuum
Pressure
Plug assist
Reverse draw
Free
Drape
Snap-back, reverse draw, billow
Matched die
Mechanical

## Slide 4: Vacuum Forming
Vacuum draws the part against the mold “cavity”

## Slide 5: Pressure Forming
Air pressure presses the sheet against the mold “cavity”
No sound

## Slide 6: Plug Assist Forming
Plug stretches the material for a more evenly distributed part

## Slide 7: Plug Assist
Plastic does not thin when in contact with the plug (or wall)

## Slide 8: Drape Forming
Mold “cavity” protrudes upward

## Slide 9: Reverse Draw Forming
Vacuum stretches material before forming for a more uniform part

## Slide 10: Snap-Back Forming
Two stage vacuum forming process
Stage one pre-stretches material
Stage two forms the material on the mold

## Slide 11: Billow Forming

## Slide 12: Matched Die Forming
Upper and lower mold “cavities” mate up or match
For greater detail
For complexity
High tolerances

## Slide 13: Mechanical Forming
No positive or negative air pressure applied to mole
All molding is done by mechanical means
There is less detail than most of the other processes

## Slide 14: Free Forming
Parts are blown
No contact with mold surfaces
Excellent optical clarity

## Slide 15
Automation

## Slide 16: Blister Pack and Skin Pack
Blister pack has space between material and packaged part
  Usually a moderately rigid material
  A mold is still needed
Skin pack sheet is held firmly against part
  Flexible materials are used
  No mold is needed

## Slide 17: Blister Pack and Skin Pack
Blister Packs
Skin Packs
Formed blister pack material

## Slide 18: Form, Fill and Seal

## Slide 19: Form, Fill, and Seal
No sound

## Slide 20: Twin Sheet Thermoforming
Thermoforming of two sheets simultaneously
Multiple colors or textures
No sound

## Slide 21: Twin Sheet Thermoforming

## Slide 22: Equipment
Machines

## Slide 23: Equipment
Machines

## Slide 24: Equipment
Machines

## Slide 25: Equipment
Machines
Blister Pack Machine
Skin Pack Machine
Vacuum Former
Shuttle Mold Machine

## Slide 26: Equipment
Molds
  Materials
    Wood
      50-100 parts
    Fiberglass
      Up to 50,000 parts
    Metal
      Millions of parts
Fiberglass mold
Metal Mold
Wooden mold (treated for longer life)

## Slide 27: Thermoforming Molds

## Slide 28: Equipment
Molds

## Slide 29: Equipment
Trimming
  Robotic trimming
  Die cutting
No sound

## Slide 30: Equipment
Plant Considerations
  Material handling
    Sheets
    Rolls
  Part handling
    Secondary processes
    Trimming
  Scrap handling
    Regrind/disposal

## Slide 31: Product Considerations
Materials
  Thermal profile
    Thermoforming does not take the material to Tm
    Material must have a Tg
    Thermal degradation is possible
  Extruded or cast sheet
  Specialty Handling
    Drying, pre-conditioning

## Slide 32: Product Considerations
Shapes and Part Design
  Undercuts
    Core pulls
  Size
    Depth, surface area

## Slide 33: Products

## Slide 34: Product Considerations
Draw Ratio (depth to width)
  Normally should not exceed 2:1 but can go to 7:1
Area Ratio (area before forming to area after forming)
  Measures the amount of thinning, for instance, 1:2 means that the material is half as thick (assuming uniform thinning)

## Slide 35: Thermoforming Part Distortion

## Slide 36: Operation and Control
Speed of vacuum application
Temperature of the mold
Size of the bubble
Plug size

## Slide 37: Thank You