## Slide 1: Rotational Molding
MFG 355

## Slide 2: Introduction
Also known as rotomolding or rotocasting
Large, hollow, one-piece plastic products
Toys (Little-Tykes)
Suitable for small and slightly complex shapes

## Slide 3: Example Products

## Slide 4: Example Products

## Slide 5: Example Products

## Slide 6: Example Products

## Slide 7: Example Products

## Slide 8: Example Product

## Slide 9: House Water Tanks

## Slide 10: World Wide Molders
One of the easiest plastics processes to begin in an under-developed country

## Slide 11: Rotomolding Overview

## Slide 12: The Process

## Slide 13: The Method - Loading
A predetermined amount of resin is loaded into the mold
The mold is closed after the flanges have been cleared of resin particles
Rotate the mold to ensure no tools have been left on the machine

## Slide 14: The Method - Heating
Rotate the mold in a high-temperature environment
The resin will always sit at the lowest point of the cavity (powder pool)
It will slowly coat the mold interior until all the resin has melted
The resin will then continue to densify as the gap between the particles disappears
Remove the mold from the oven when the powder has completely melted and densified

## Slide 15: The Method - Cooling
Rotate the mold in a room temperature environment
This allows the layer of resin to cool and solidify
Water can also be used, but care should be exercised

## Slide 16: The Method - Unloading
Remove the clamping system
“Pry” open the mold
Lift the completed, hollow, one-piece part from the mold.
Repeat the cycle

## Slide 17: Process Comparisons
Strengths
  Small production runs
  Large part capability
  Low tooling costs
  ‘Stress-free” products
  Short product development lead times

## Slide 18: Process Comparisons
Weaknesses
  Slow cycle times
  Limited material choices
  Difficult to automate
  Poor image
  Low technology culture

## Slide 19: Materials

## Slide 20: The Materials
Low Zero Shear Viscosity is required to aid in the flow of the polymer within mold
MFI
  Lower MFI resins – high strength products
  Higher MFI – good surface finish and surface detail

## Slide 21: The Materials
Particle shape and size is crucial to the flow characteristics as the mold is rotating
  Standard size is a 35 mesh powder (500 micron, 0.0197 inches)

## Slide 22: The Materials
Other Material
  Foams
    Post-process
    In-process
  Liquid reactive polymers
  Micro-pellets
  Additives
  Ceramics

## Slide 23: Fixed Carousel Machines

## Slide 24: Independent Carousel Machines

## Slide 25: Rock-and-Roll Machines

## Slide 26: Rock-and-Roll Machines

## Slide 27: Clamshell Machines

## Slide 28: Shuttle Machines

## Slide 29: The Molds
Materials
  Steel
    Mild
    Stainless
  Aluminum
    Cast
    Machined
    Plate

## Slide 30: The Molds – Frame and Spider

## Slide 31: The Molds - Parting Line

## Slide 32: The Molds - Mold Sections

## Slide 33: The Molds - Clamping Hardware

## Slide 34: The Molds - Vents

## Slide 35: The Molds - Vents

## Slide 36: The Molds – Kiss-Offs

## Slide 37: The Molds - Threads

## Slide 38: The Molds - Inserts

## Slide 39: The Method
The concern
  How do you really know when it is time to do the next step?
    When is the resin melted?
    When is it cooled?
  In the early 90’s, QUB invented an instrument that revolutionized process comprehension and control
    The Rotolog™

## Slide 40: The Method – Rotolog™

## Slide 41: The Method – Rotolog™

## Slide 42: The Method – Temperature Profiles

## Slide 43: The Method – IAT Profile

## Slide 44: The Method – IAT Profile

## Slide 45: The Method – IAT Profile

## Slide 46: The Method – IAT Profile

## Slide 47: The Method – IAT Profile

## Slide 48: The Method – IAT Profile

## Slide 49: The Method – IAT Profile
We can thus observe:
When powder first sticks to the mold
When the powder has been consumed
When optimal melt sintering has occurred
When solidification is occurring
When the plastic separates from the mold
A
B
C
D
E

## Slide 50: The Method – IAT Profile
The Peak Internal Air Temperature (PIAT) is the key process control parameter and is independent of all other process variables (point C)
C

## Slide 51: Conclusion
Though in a state of infancy, Rotomolding offers unique advantages over other plastics processes
There are endless opportunities for research and development
Rotomolding has a very promising future, more so than many competing processes

## Slide 52
Thank You