## Slide 1: Casting
MFG 355

## Slide 2: Types of Casting
Mold Casting
Embedding
Encapsulation
Dip Casting
Fluidized bed coating
Painting
Slush casting
Static power casting
Cell casting
Continuous casting
Film casting

## Slide 3: Mold Casting
Open mold
Closed Mold

## Slide 4: Mold Casting

## Slide 5: Mold Casting
Low pressure
  You can use flexible molds
  It is easy to get undercuts and intricate details that are more difficult in some of the other processes

## Slide 6: Open Casting of PU

## Slide 7: Encapsulation/Embedding
Cover a finished part with resin
  Physical protection
  Electrical barrier
  Weathering protection
Step 1
Step 2

## Slide 8: Acrylic Encapsulation
The acrylic needs to be crosslinked for best results
Crosslinking needs a carbon-carbon double bond (additional reaction)
Mixing the monomer and the polymer gives the correct viscosity and will allow crosslinking if a crosslinking agent is also added

## Slide 9: Acrylic Encapsulation
+
)n
(
Polymer
Monomer
+
Triallyl cyanurate (TAC)
+
Peroxide

## Slide 10: Acrylic Casting

## Slide 11: Dip Casting
Dip a part or mold into liquid resin
Resin can be it’s own part (gloves) or it can be a portion of a larger part

## Slide 12: Fluidized Bed Coating
Resin used is in powder form
Resin sits in a fluidized bed
A heated part is dipped into the fluidized bed of resin and the part is encapsulated/coated with resin
The part is then put in an oven to sinter the resin powder

## Slide 13: Painting
Generally applied in liquid form
Generally done for protection from the environmental factors

## Slide 14: Slush Casting
Similar to Rotational Molding
  Slush (instead of powder) poured into mold
    Slush is made from a mixture of resin and plastisols
  Mold rotated and tipped
  Part forms on surface of mold
  Extra slush poured free
  Part removed

## Slide 15: Static Powder Casting
Static is used instead of a plastisol to help the plastic coat the mold
Preset static charge will help to create a determined wall thickness
Any excess that is not held to the walls of the mold long enough for fusion is dumped out of the mold

## Slide 16: Cell Casting
Syrup (acrylic) is poured between to sheets of glass
Glass is held apart by a gasket that keeps syrup between the glass sheets
Syrup is allowed to dry with no disturbances (there are no residual stresses—mostly)
  Transparency increases greatly

## Slide 17: Cell Casting

## Slide 18: Monterey Bay Aquarium
The main viewing window (acrylic) into the Outer Bay exhibit is 56.5 feet long, 17 feet tall, and 13 inches thick, and weighs 78,000 pounds!

## Slide 19: Continuous Casting
Built off of the concept of cell casting
Higher production rates
Gasket
Liquid Resin
Stainless Steel Belt
Stainless Steel Belt
Cast Sheet

## Slide 20: Film Casting
Similar to continuous casting method
Solvent Recovery
Heaters
Casting Solution
Spray onto
belt
Stainless Steel Belt
Take-Up Roller

## Slide 21: Machine Types
Low pressures
Low temperatures
No specific equipment required other than what is necessary for the individual mold

## Slide 22: Molds
Almost any solid material
Any porous material must be sealed from resin absorption for part quality
Major mold considerations:
  Durability
  Ease of fabrication
  Convenience
  porosity

## Slide 23: Plant Concepts
Plant layout is a function of the size of parts to be made and any automation that may be employed

## Slide 24: Materials
Acrylic syrup
Polyester (thermoset) resins
Phenolics
Epoxy resins
Polyurethanes
Silicones
Vinyls
Hot melt casting resins

## Slide 25: Shapes and Part Design
Jewelry
Optical lenses
Tool handles
Knobs
Countertops
Sinks
Buttons

## Slide 26: Thank You